Special Maintenance Warning Signals
Code	Meanings	Flash Times	Possible problem	Solution

1	Throttle malfunction	3 3	Throttle is not return	Loose the throttle or replace it
2	Skid state	1 1	The skid switch already puts through	Loose brake handle or replace it
3	Handle malfunction	1 2	Throttle is damaged	Check the cables of throttle or replace it
4	Overvoltage protection	1 5	Battery's voltage is exceed, must have been used the wrong battery pack.	Replace the battery pack

5	Low voltage	1 4	Battery's voltage is too low	Charge battery
6	Hall disconnection	3 1	Motor Hall disconnection	Examine motor Hall connection or replace the motor
7	Current sensor malfunction	3 2	Current sensor malfunction	Examine and repair or trigger the key switch again.
8	Motor limites the current	0 3	Motor is in a heavy load	Lightens load.
9	Battery limites the current	0 2	Motor is in a heavy load	Lightens load.
10	Protection for avoid overheating	2 3	Temperature protection	normal conditions, restores after temperature reducing
11	Deeply lack voltage	1 3	Battery's voltage is too low	System is in the lack voltage protecting condition ,the battery needs to be charged.

12	Motor been locked rotor	2 1		Release loads , cancel locked rotor
13	Protection for avoid System output short circuit	2 2		Eliminate malfunction of the motor short circuit , examine the system output connection

14	Light is always on	System works well.
15	Light is always off	LED light breaks down , no power or some parts were damaged , pls check the LED light and the power.
16	Others	Malfunction, examine and repair system .